## Slide 1
Adaptive EMS Calibration
Using EEG-Based Deep Learning Classification
Methods & Results Summary
31
Participants
160
Trials / Subject
4
EMS Conditions
5
DL Models

## Slide 2
What is this study about?
The Problem: EMS (Electrical Muscle Stimulation) delivers electrical currents to muscles. Tolerance levels differ hugely between people. Currently, calibration is done manually by trial and error, which is slow and inconsistent.
Goal
Detect when EMS stimulation becomes intolerable using brain signals, so a computer system can automatically adjust the intensity in real time.
Approach
Record EEG (brainwaves) while participants receive EMS at 4 levels: no stimulation, minimum, medium, and maximum intensity.
Why EEG?
EEG captures the brain's immediate response to stimulation non-invasively from the scalp in real time.

## Slide 3
Experiment Design
4 EMS Conditions
S4 — No Stimulation
Sham / Baseline
S1 — Minimum Intensity
Just perceivable
S2 — Medium Intensity
Clearly perceivable
S3 — Maximum Intensity
Intolerable / painful
40 trials per condition · 160 total per subject · 31 subjects
Trial Timeline
Rest period
2.5–3.5 s
(randomised)
EMS stimulation
1 s
Post-stim window
0.5 s
Self-report
1–3 s
(S5–S9)
← Epoch window for analysis: −2.0 s to +1.5 s →
Setup & Protocol
EEG Cap:
64-channel BrainProducts system, CACS-64 montage, FCz online reference
EMS Device:
Teslasuit delivering calibrated current to left hand
Staircase Protocol:
Part 1 identifies each participant's personal thresholds
Main Task:
Part 2 presents 160 randomised trials across the 4 conditions

## Slide 4
EEG Preprocessing Pipeline
1
Load Raw Data
Read .vhdr/.eeg/.vmrk BrainVision files via MNE-Python..
2
Drop Channels
Remove 4 peripheral electrodes (FT9, FT10, TP9, TP10).
4
Band-pass Filter 1–100 Hz
Remove slow drift (< 1 Hz) and high-frequency noise (> 100 Hz).
5
Notch Filter 50 Hz
Remove power-line interference
6
Re-reference (CAR)
Recover the FCz online reference electrode, then apply Common Average Reference
7
Epoch + Baseline Correct
Cut 160 clips of −2.0 s to +1.5 s around each EMS marker. Apply baseline correction using −0.7 s to −0.2 s window.
Output: X matrix (n_epochs × 60 channels × 750 time-points) + y vector (0 = no stim · 1 = min · 2 = medium · 3 = max)

## Slide 5
Classification Methodology
Within-Subject Paradigm: A completely separate model is trained for each participant. This is essential because EMS tolerance is deeply personal (what is painful for one person may feel mild to another).
EEGNet
EEGNetv4 (braindecode)
What it does: A compact convolutional neural network designed specifically for EEG. Uses depthwise convolutions to learn spatial patterns across electrodes, then temporal patterns across time.
Why chosen: Works well with limited data (160 trials). Widely used as a benchmark in EEG classification research.
ShallowNet
ShallowFBCSPNet (braindecode)
What it does: A shallow convolutional network that applies a single temporal convolution followed by a spatial filter, inspired by classical EEG signal processing (FBCSP).
Why chosen: Captures oscillatory EEG features in specific frequency bands. Strong for motor and sensory paradigms.
Cross-Validation & Training
Repeated Stratified K-Fold: 5 folds × 5 repeats = 25 total evaluations per model per subject
Baseline removal before input: only the 0 s → +1.5 s window is fed to the classifier
Z-score normalisation computed from training data only
Early stopping: training halts if validation loss does not improve for 15 consecutive epochs

## Slide 6
Results Overview (EEGNet and ShallowNet)
54.7%
EEGNet group mean
Chance = 25%
44.2%
ShallowNet group mean
Chance = 25%
22 / 31
Subjects above 50%
using EEGNet
29 / 31
EEGNet wins
vs ShallowNet
25% chance
EEG Net
ShallowNet

## Slide 7
Results Overview
54.9%
EEGNet
±11.4% across subjects
53.9%
EEGInception
±10.8% across subjects
46.7%
EEGConformer
±10.4% across subjects
44.4%
ShallowNet
±10.4% across subjects
42.6%
ATCNet
±9.4% across subjects

## Slide 8
Results Overview
Confusion Matrix