## Slide 1
DECODING STIMULATION INTENSITY FROM EEG
Time-domain & frequency-domain decoding of EMS haptic-shock intensity,
comparing shrinkage-LDA, EEGNet, and a 4-family stacking ensemble.
29 subjects · 60 channels · 3-class · 4-class · stacking · LOSO + within-subject

## Slide 2
DATA COLLECTION
How the EEG was recorded & prepared
60
EEG channels
10-20 montage, central/fronto-central focus for the somatosensory response
1000 Hz
Acquisition rate
Notch-filtered at 50 Hz; band-pass up to 100 Hz on the raw recording
250 Hz
Analysis rate
Anti-aliased decimation by 4 (FIR low-pass) before feature extraction
160
Epochs / subject
Stimulus-locked trials, balanced across intensity conditions
Preprocessing & epoching pipeline
Raw EEG
1000 Hz · notch 50 · BP 100
›
Downsample ÷4
→ 250 Hz, anti-aliased
›
Epoch
stimulus-locked
›
Crop window
−0.2 → +1.5 s
›
Label scheme
3-class / 4-class
**Note: 31 subjects were recorded, but subjects 10 and 24 have been removed from training sets.

## Slide 3
Part 1: EEGNet
A compact convolutional network learning its own filters from raw EEG

## Slide 4
EEGNET · 3-CLASS
Network, setup, and performance
Architecture (EEGNet-8,2)
Input
60 ch × T samples × 1
Temporal conv
F1 = 8 filters, kernel 500 ms
Depthwise conv
D = 2 (spatial, per-channel)
Separable conv
F2 = 16 filters
Pooling
avg-pool ×4 then ×8
Dropout
0.25 (cross) / 0.50 (within)
Head
dense → softmax
Training setup
Optimizer
Adam, lr 1e-3, batch 32
Epochs
up to 500, early-stop pat. 50
LR schedule
halve on plateau (pat. 20)
Class weights
balanced
Scaler / seed
per-channel z-score · 42
Results & reading
63.4%
within-subject
59.8%
LOSO
1.79×
vs chance (33%)
no-stim best separated (71% recall); the intermediate (min+medium merged) class is the hardest, bleeding into no-stim. LOSO ≈ within shows the model generalizes across subjects but plateaus at the same place the LDA does.

## Slide 5
EEGNET · 4-CLASS
Network, setup, and performance
Architecture (EEGNet-8,2)
Input
60 ch × T samples × 1
Temporal conv
F1 = 8 filters, kernel 500 ms
Depthwise conv
D = 2 (spatial, per-channel)
Separable conv
F2 = 16 filters
Pooling
avg-pool ×4 then ×8
Dropout
0.25 (cross) / 0.50 (within)
Head
dense → softmax
Training setup
Optimizer
Adam, lr 1e-3, batch 32
Epochs
up to 500, early-stop pat. 50
LR schedule
halve on plateau (pat. 20)
Class weights
balanced
Scaler / seed
per-channel z-score · 42
Results & reading
53.0%
within-subject
49.7%
LOSO
1.99×
vs chance (25%)
min ↔ medium collapse. Recall is 41% (min) and 34% (medium) — the two adjacent low-intensity classes look alike in EEG. no-stim (68%) and max (55%) stay best separated.

## Slide 6
Part 2: Shrinkage LDA
Hand-built ERP & band-power features → linear discriminant analysis

## Slide 7
LDA · 3-CLASS
Features, pipeline, and per-model performance
Validation pipeline
features → StandardScaler → shrinkage-LDA
Leakage-safe: extractors use no labels; scaler & LDA fit inside each fold. LOSO adds per-subject z-scoring. Artifact filter drops high baseline-SD trials.
LOSO (cross-subject)
57.8 / 58.3 / 61.7
ERP / BP / Combined %
Within-subject
62.5 / 68.1 / 71.0
ERP / BP / Combined %
Combined wins both. Band-power alone edges ERP; fusing them adds ~3 pts. Best cross-subject result of any model here.
Three feature pipelines
ERP (time)
Peak amplitude/latency & mean-window features on 8 central channels — the evoked SEP.
Band-power (freq)
log Welch PSD in delta/theta/alpha/beta/gamma across all 60 channels — the induced response.
Combined
ERP ⊕ band-power concatenated — distinct neural phenomena, non-redundant features.

## Slide 8
LDA · 3-CLASS · 7-CHANNEL DEVICE
Does a deployable montage hold up?
The 7-channel montage
Chosen from fold-stable feature importance: the fronto-central cluster where the somatosensory response concentrates.
FCz
Fz
FC2
FC4
Cz
C2
C4
60 channels vs 7 channels (LOSO)
61.7%
full 60ch
59.8%
7ch device
Only 1.9 points lost dropping from 60 channels to 7. The intensity signal is concentrated, not spread, so the montage is cheap.
7ch is 1.79x chance (33%).
LOSO (cross-subject)
61.7% → 59.8%
60ch → 7ch
Within-subject
71.0% → 68.1%
60ch → 7ch
Under 2 pts lost. 7 fronto-central channels retain ~97% of full-montage LOSO accuracy.

## Slide 9
LDA · 3-CLASS · BALANCED (40/40/40)
Removing no-stimulation: the pure-intensity question
40 / 80 / 40 (with no-stim)
Includes an easy stim-vs-no-stim contrast; the "medium" class is min+medium merged. erp+bp: LOSO 62.8% / 59.9% balanced.
40 / 40 / 40 (balanced)
no_stimulation dropped; min vs medium vs max only. erp+bp: LOSO 58.0% / 58.1% balanced, within-subject 69.0%.
What it proves
Only a modest drop without the easy class — the decoder genuinely separates graded intensity, not just whether a pulse occurred.
Balancing to 40/40/40 isolates the real question — discriminating stimulation levels. Chance is a clean 33%, so accuracy is directly interpretable with no majority-class caveat.

## Slide 10
LDA · 4-CLASS
Features, pipeline, and per-model performance
Three feature pipelines
ERP (time)
Peak amplitude/latency & mean-window features on 8 central channels — the evoked SEP.
Band-power (freq)
log Welch PSD in delta/theta/alpha/beta/gamma across all 60 channels — the induced response.
Combined
ERP ⊕ band-power concatenated — distinct neural phenomena, non-redundant features.
Validation pipeline
features → StandardScaler → shrinkage-LDA
Same leakage-safe design. 4th class (min_intensity) is the only difference — it sits between no-stim and medium.
LOSO (cross-subject)
44.8 / 44.2 / 48.7
ERP / BP / Combined %
Within-subject
50.8 / 58.0 / 61.6
ERP / BP / Combined %
Combined still best. Cross-subject the extra class costs ~13 pts vs 3-class; the min↔medium overlap is the ceiling.

## Slide 11
LDA · 4-CLASS · 7-CHANNEL DEVICE
Does a deployable montage hold up?
The 7-channel montage
Chosen from fold-stable feature importance: the fronto-central cluster where the somatosensory response concentrates.
FCz
Fz
FC2
FC4
Cz
C2
C4
60 channels vs 7 channels (LOSO)
48.7%
full 60ch
47.3%
7ch device
Only 1.4 points lost dropping from 60 channels to 7. The intensity signal is concentrated, not spread, so the montage is cheap.
7ch is 1.89x chance (25%).
LOSO (cross-subject)
48.7% → 47.3%
60ch → 7ch
Within-subject
61.6% → 57.2%
60ch → 7ch
Same story as 3-class. Dropping to 7 channels costs ~1.4 pts cross-subject. min↔medium overlap stays the ceiling.

## Slide 12
WHAT DIDN'T WORK
Approaches tested and rejected
Time-frequency (ERD/ERS)
erp+bp+tf -> LOSO 57.4% (vs 62.8%). The 1200 ERD/ERS features dilute the model; the time-frequency domain is less discriminative than time or frequency alone.
Riemannian covariance
riem alone LOSO 57.5%; concatenated with erp+bp 59.7% — both below the 62.8% baseline. As a single feature block it only dilutes.
Selection & montage
Nested-CV feature selection across erp+bp+tf never beat erp+bp (best 60.1% vs 59.9%). The XON frontal-parietal montage was far worse (46.9%).
The recurring failure mode is dilution: with ~120-160 trials/subject, piling features into one vector hurts cross-subject accuracy. erp+bp is the ceiling of single-vector linear feature engineering.

## Slide 13
Part 3: Stacking ensemble
Fusing per-family LDAs at the decision level — the best model

## Slide 14
STACKING · 3-CLASS · BEST MODEL
Per-family LDAs fused by a meta-learner
Architecture
One shrinkage-LDA per family (ERP, band-power, ERD/ERS, Riemannian). A logistic meta-learner fuses their class probabilities based on correctness during learning.
Results
Within 73.0% / 70.2% bal, LOSO 66.7% / 63.0% bal. This is +3.9 / +3.1 over erp+bp, which is the only method that beats it.
Why it works
The weaker but complementary views help when they’re fused after decision, not concatenated pre inference, as their errors decorrelate from ERP/band-power. Meta-weights (LOSO): erp .37 / bp .32 / riem .20 / tf .11.
Decision-level fusion beats feature concatenation. Riemannian features here earn some real weight in the ensemble. The gain is concentrated in LOSO, the cross-subject metric that matters.

## Slide 15
WHY THE META-LEARNER'S WEIGHTS ARE NEUROSCIENCE
Decision Weighting
Presence ← ERP + gamma BP
With no stim, there is no evoked potential and no induced gamma so the absence of both the is the cleanest evidence that no afferent volley reached cortex, so the two strong markers dominate.
Max intensity ← induced gamma
The strongest input drives the gamma response in sensorimotor cortex as per Wanjoo’s observations (gamma power scales with stimuli), so the spectral marker becomes the most diagnostic signal for high intensity.
Medium class is ambiguous
For the middle class, every weight is small (<=+0.62), as no marker is confident. The trace exposes the difficulty and matches where the confusion matrix concentrates.

## Slide 16
A BACKTRACK
Trace of a no-stim trial
End-to-end decision calculation
decision = SUM (meta-weight x family vote)
family vote = SUM (LDA coef x feature)
feature = a named amplitude/band at a named electrode & latency
One trial (true: no-stim)
erp 0.82 (no SEP) · bp 0.58 (no induced gamma) · riem 0.98 (no network engagement) but tf votes 0.58 medium (incorrectly), fooled by baseline-rhythm fluctuation, a known weakness of single-trial ERD.
Principled override
The three independent, reliable markers carry more weight and agree; the meta-learner's low tf weight (.11) reflects its unreliability in this area.
tf is fooled because ERD is defined relative to baseline, and sensorimotor rhythms dip spontaneously, so it read a random baseline wobble as a stimulus response. For this reason, the ensemble model’s multi-decisional architecture is capable of providing weight to different features for different class-trials, enhancing explainability by improving the model’s decisions in all regions by electing the most trusting candidate.

## Slide 17
STACKING · 2-CLASS · TOLERABLE vs INTOLERABLE
Detecting high-intensity (intolerable) stimulation
The reframing
Bottom three intensities merged into 'tolerable' (120) vs 'intolerable' (40). The 75/25 imbalance is handled with uniform LDA priors + a class-balanced meta-learner (Options 1 & 2).
Results
LOSO 79.9% balanced · within 87.3%. ROC-AUC 0.88 / 0.94. Intolerable recall 0.80 (LOSO). The minority class is genuinely detected, not ignored (majority baseline 75%).
What marks intolerable
Elevated fronto-central gamma-band power and a larger central evoked-potential (SEP) amplitude (both known to scale with stimulus intensity) are the top discriminators.
Collapsing to tolerable vs intolerable cleanly separates high-intensity EMS (cross-subject ROC-AUC 0.88) and surfaces its neural signature — the basis for a discomfort-aware stop trigger.

## Slide 18
X.ON DEVICE · 60 TO 7-CHANNEL REDUCTION
7 electrodes: a deployable montage without losing fidelity
The reduction
60 -> 7 channels (F3, F4, C3, Cz, C4, P3, P4). Feature count 3434 -> 294 (12x smaller): erp 91, bp 35, tf 140, riem 28. Identical 4-family stack, every family restricted to the 7 electrodes.
Impact on performance
LOSO accuracy 64.0% (balanced 59.8%) vs the full 60-channel stack's 66.7% (balanced 63.0%). Within-subject 69.1% vs 73.0%. Only ~2-3 pts lost.
Still practical & robust
The meta-learner re-balances for 7 channels. Riem rises to 0.26 as its 28-feature covariance is now clean and low-dimensional. Same adjacent-intensity confusion; the within-subject sweep runs in ~20s.
A wearable headset needs few electrodes. The X.on 7-channel montage keeps the decoding fidelity of the full cap while being far cheaper and faster to acquire.

## Slide 19
FUNCTIONAL CONNECTIVITY · PHASE COUPLING
Do FC/C/P regions phase-lock differently with intensity?
The method
Phase-locking (PLV) and volume-conduction-robust iPLV between FC / C / P regions, per band, per intensity — filter-Hilbert phase across trials, baseline-corrected, Friedman-tested over 29 subjects.
The finding
Low-frequency (delta/theta/alpha) inter-region coupling RISES dose-dependently with intensity (delta FC-C: +0.028 -> +0.064 -> +0.099); gamma coupling FALLS. Significant at p~0, robust to volume conduction.
Why it matters
Stronger EMS drives widespread low-frequency phase synchronization across the sensory network — an interpretable, physiologically-named measure of network engagement (vs opaque Riemannian covariance).
This becomes the per-trial 'conn' feature family: region-pair PLV/iPLV per band = 60 interpretable features (vs Riemannian's 1830).

## Slide 20
FINAL MODEL · 5-FAMILY STACK
Adding phase connectivity to the ensemble, the best decoder
The model
Five per-family LDAs fused by the meta-learner: ERP, band-power, ERD/ERS, Riemannian covariance, and phase connectivity (conn). Same leakage-safe LOSO protocol, all 60 channels.
Results
LOSO 68.1% / 64.8% balanced — the project's best. +1.8 balanced over the 4-family stacks, and ~+5 over the erp+bp baseline (chance 33%).
Why 5 helps
Connectivity and Riemannian are complementary, not redundant — the meta-learner keeps BOTH (conn 0.25, riem 0.14). Phase-locking and covariance capture partly different spatial structure.
The connectivity work yields a marginal but real gain — the 5-family stack is the new best model. conn alone also matches riem using 30x fewer, interpretable features.